## Slide 1: Організації підмереж IP-мережі Планування адресного простору
Поділ на підмережі з метою забезпечення ефективного використання адресного простору
Підмережі в IPv4 мережі
Питання проектування IPv6 мереж

## Slide 2: Network Segmentation Reasons for Subnetting
Large networks need to be segmented into smaller sub-networks, creating smaller groups of devices and services in order to:
Control traffic by containing broadcast traffic within subnetwork
Reduce overall network traffic and improve network performance
Subnetting - process of segmenting a network into multiple smaller network spaces called subnetworks or Subnets.
Communication Between Subnets
A router is necessary for devices on different networks and subnets to communicate.
Each router interface must have an IPv4 host address that belongs to the network or subnet that the router interface is connected to.
Devices on a network and subnet use the router interface attached to their LAN as their default gateway.
Notes: 9.1 Subnetting an IPv4 Network
9.1.1 Network Segmentation
9.1.1.1 Reasons for Subnetting
9.1.1.2 Communication Between Subnets

## Slide 3: Subnetting an IPv4 Network IP Subnetting is FUNdamental
Notes: 9.1.2 IP Subnetting is FUNdamental
9.1.2.1 The Plan
9.1.2.2 The Plan - Address Assignment

## Slide 4: Subnetting an IPv4 Network Basic Subnetting
Borrowing Bits to Create Subnets
Borrowing 1 bit 21 = 2 subnets
Subnet 1
Network 192.168.1.128-255/25
Mask: 255.255.255.128
Subnet 0
Network 192.168.1.0-127/25
Mask: 255.255.255.128
Borrowing 1 Bit from the host portion creates 2 subnets with the same subnet mask
Notes: 9.1.3 Subnetting an IPv4 Network
9.1.3.1 Basic Subnetting

## Slide 5: Subnetting an IPv4 Network Subnets in Use
Subnet 0
Network 192.168.1.0-127/25
Subnet 1
Network 192.168.1.128-255/25
Notes: 9.1.3.2 Subnets in Use

## Slide 6: Subnetting an IPv4 Network Subnetting Formulas
Calculate Number of Subnets
Calculate Number of Hosts
Notes: 9.1.3.3 Subnetting Formulas

## Slide 7: Subnetting an IPv4 Network Creating 4 Subnets
Borrowing 2 bits to create 4 subnets. 22 = 4 subnets
Notes: 9.1.3.4 Creating 4 subnets

## Slide 8: Subnetting an IPv4 Network Creating 8 Subnets
Borrowing 3 bits to Create 8 Subnets. 23 = 8 subnets
Notes: 9.1.3.5 Creating 8 subnets

## Slide 9: Subnetting an IPv4 Network Creating 8 Subnets(continued)
Notes: 9.1.3.5 Creating 8 Subnets (continued)

## Slide 10: Determining the Subnet Mask Subnetting Based on Host Requirements
There are two considerations when planning subnets:
Number of Subnets required
Number of Host addresses required
Formula to determine number of useable hosts
  2^n-2
  2^n (where n is the number the number of host bits remaining) is used to calculate the number of hosts
  -2 Subnetwork ID and broadcast address cannot be used on each subnet
Notes: 9.1.4 Determining the Subnet Mask
9.1.4.1 Subnetting based on Host Requirements

## Slide 11: Determining the Subnet Mask Subnetting Network-Based Requirements
Calculate number of subnets
Formula 2^n (where n is the number of bits borrowed)
Subnet needed for each department in graphic
Notes: 9.1.4.2 Subnetting Network-Based Requirements

## Slide 12: Determining the Subnet Mask Subnetting To Meet Network Requirements
It is important to balance the number of subnets needed and the number of hosts required for the largest subnet.
Design the addressing scheme to accommodate the maximum number of hosts for each subnet.
Allow for growth in
each subnet.
Notes: 9.1.4.3 Subnetting to Meet Network Requirements

## Slide 13: Determining the Subnet Mask Subnetting To Meet Network Requirements (cont)
Notes: 9.1.4.4 Subnetting to Meet Network Requirements (Cont)

## Slide 14: Benefits of Variable Length Subnet Masking Traditional Subnetting Wastes Addresses
Traditional subnetting - same number of addresses is allocated for each subnet.
Subnets that require fewer addresses have unused (wasted) addresses. For example, WAN links only need 2 addresses.
Variable Length Subnet Mask (VLSM) or subnetting a subnet provides more efficient use of addresses.
Notes: 9.1.5 Benefits of Variable Length Subnet Masking
9.1.5.1 Traditional Subnetting Wastes Addresses
9.1.5.2 Variable Length Subnet Mask (VLSM)

## Slide 15: Benefits of Variable Length Subnet Masking Variable Length Subnet Masks (VLSM)
VLSM allows a network space to be divided in unequal parts.
Subnet mask will vary depending on how many bits have been borrowed for a particular subnet.
Network is first subnetted, and then the subnets are subnetted again.
Process repeated as necessary to create subnets of various sizes.
Notes: 9.1.4.2 Variable Length Subnet Masks (VLSM)

## Slide 16: Benefits of Variable Length Subnet Masking Basic VLSM
Notes: 9.1.5.3 Basic VLSM

## Slide 17: Benefits of Variable Length Subnet Masking VLSM in Practice
Using VLSM subnets, the LAN and WAN segments in example below can be addressed with minimum waste.
Each LANs will be assigned a subnet with /27 mask.
Each WAN link will be assigned a subnet with /30 mask.
Notes: 9.1.5.4 VLSM in Practice

## Slide 18: Benefits of Variable Length Subnet Masking VLSM Chart
Notes: 9.1.5.5 VLSM Chart

## Slide 19: Structured Design Planning to Address the Network
Allocation of network addresses should be planned and documented for the purposes of:
Preventing duplication of addresses
Providing and controlling access
Monitoring security and performance
Addresses for Clients - usually dynamically assigned using Dynamic Host Configuration Protocol (DHCP)
Sample Network Addressing Plan
Notes: 9.2 Addressing Schemes
9.2.1 Structured Design
9.2.1.1 Planning to Address the Network
9.2.1.2 Assigning Addresses to Devices

## Slide 20: Subnetting an IPv6 Network Subnetting Using the Subnet ID
An IPv6 Network Space is subnetted to support hierarchical, logical design of the network
Notes: 9.3 Design Considerations for IPv6
9.3.1 Subnetting an IPv6 Network
9.3.1.1 Subnetting Using the Subnet ID

## Slide 21: Subnetting an IPv6 Network IPV6 Subnet Allocation
Notes: 9.3.1.2 IPv6 Subnet Allocation

## Slide 22: Subnetting an IPv6 Network Subnetting into the Interface ID
IPv6 bits can be borrowed from the interface ID to create additional IPv6 subnets
Notes: 9.3.1.3 Subnetting into the Interface ID

## Slide 23: Висновки
IP рішення можуть бути адаптовані до потреб проектування мережі за допомогою маски підмережі.
Безкласове розбиття на підмережі забезпечує більшу гнучкість за допомогою маски підмережі змінної довжини.
Subnetting a subnet, or using Variable Length Subnet Mask (VLSM) was designed to avoid wasting addresses.
IPv6 address space is a huge address space so it is subnetted to support the hierarchical, logical design of the network not to conserve addresses.
Size, location, use, and access requirements are all considerations in the address planning process.
Notes: Chapter 9 Summary

## Slide 24: Висновки
IP рішення можуть бути адаптовані до потреб проектування мережі за допомогою маски підмережі.
Безкласове розбиття на підмережі забезпечує більшу гнучкість за допомогою маски підмережі змінної довжини.